## Slide 1
EXEMPLARY LANDSCAPE STUDY- POLYETHYLENE FURANOATE (PEF)
POLYETHYLENE FURANOATE (PEF)

## Slide 2: Contents
Introduction to PEF
Applications and Growth Prospects of PEF
Key Developments Related to Bio-Based polymers
Objectives for the Landscape Study
Trend Analysis and Graphical Representation
Key Technology Trends
Patent Portfolio Analysis – Technological Dissection of Patent Portfolio and Analysis of Key Granted Patents
Recycling Technologies for PEF
Analysis of Key Granted Patents Assigned to Educational Institutes and Universities
Appendix A – Sources
Appendix B – Definition of IPC Classes

## Slide 3: Introduction- Polyethylene Furanoate (PEF)
What is PEF?
PEF is a 100% recyclable bio-based polymer derived from plants having the potential to replace the plastic industry’s giant polyethylene terephthalate (PET), which is a durable material derived from conventional resources.
It can be referred as the next generation polyester,
having better mechanical and barrier properties than
the current biggest selling polyester (PET).
PEF V/S PET
PEF has very good barrier properties (hard to achieve with most bio-based polymers)
O2 barrier – 6 times greater than PET
CO2 barrier – 3 times better than PET
H2O barrier – 2 times better than PET
Better tensile strength
PEF requires less additives than PET
For sources of information, please refer to Appendix 1

## Slide 4: Introduction- Polyethylene Furanoate (PEF)
4) PEF also has interesting mechanical properties compared to PET.
Higher Tg (glass transition temperature)
Lower Tm (melting point)
Higher modulus
5) PEF can be recycled and incorporated into the PET recycle streams at up to 5% PEF with no affect on the recycled PET performance.
6) Permits greater light weighting and superior thermal stability without heat-setting (can be hot filled at about 200-deg F).
Applications of PEF
PEF Bottles- Water bottle, beverage bottle etc
PEF Fibers- Apparels, carpets, home furnishing, disposables commodities, fabrics, diapers, filters and industrial fibres
PEF Films
For sources of information, please refer to Appendix 1

## Slide 5: Growth Prospects for PEF
Avantium developed and patented YXY technology platform aimed at manufacturing bio fuels, bio based plastics and bio chemicals.
Avantium established strategic partnership with Danone, Coca-Cola and ALPLA for developing and commercializing bio-based polymers derived from PEF.
In 2014, Avantium, Danone, Swire Pacific and Coca-Cola signed a consortium of USD 50 million investments aimed at developing and commercializing the alternative to PET for packaging applications.
In 2014, Avantium demonstrated the application of PEF for manufacturing of fibers to make 100% bio based t-shirts for textile manufacturers.
Asia Pacific is likely to be a lucrative market in the near future on account of growing packaging industry in India and China in vague of positive outlook on food & beverage, consumer goods and pharmaceutical sectors.
North America is likely to be promising market for bio based chemicals in light of increasing environmental concerns towards reducing GHG emissions coupled with stringent regulations towards non-recyclable plastic consumption at domestic level.
For sources of information, please refer to Appendix 1

## Slide 6: Key Developments Related To Bio-Based Polymers
2009
PlantBottle™ by Coca-Cola (DTCC) - first ever recyclable PET beverage bottle introduced in the market
Toray - Gevo partnership succeeded in producing fully renewable biobased PET
Coca-Cola announced its agreement with Virent, Gevo and Avantium, companies which are plant based polymer manufacturers
Avantium officially opened PEF pilot plant in Geleen, Netherlands
Coca-Cola, Ford, Heinz, NIKE, and P & G announced the formation of Plant PET Technology Collaborative (PTC), for development and use of 100% plant-based PET materials and fibre
2014
Avantium closed a financing
round of $50 million from a consortium of Swire Pacific, Coca-Cola, DANONE, ALPLA, and existing shareholders
Avantium plans to start commercial production of FDCA and PEF in 2016 through a 50,000 tons/year plant
For sources of information, please refer to Appendix 1
June 2011
Dec 08 2011
Dec 15 2011
June
2012
2016

## Slide 7: Objectives of the Landscape/Study
To understand technology and prepare patent landscape
To understand major patent holders, geographical distribution of patents, top sub-technologies based on IPC codes
Analysis of patent filing trends over the years, top assignees, top patent classifications, among others
To conduct Patent Portfolio based study of patents relating to core focus area of PEF in the patents/ applications
To understand the recycling technology of PEF and Novelty Features of all Granted Patents pertaining to PEF
Report provides patent analysis for PEF market, which includes study of recycling of PEF, applications, and advance technology based patents
The landscape study focuses on patents pertaining to PEF filed between 2005-2015
Assumptions:
For sources of information, please refer to Appendix 1

## Slide 8: Filing Trends - Overall
Application Year
No. of Patent
Applications
Insights
Chart: 
| WO | US | CN | EP | JP | CA | MX
Count | 68 | 65 | 45 | 37 | 30 | 18 | 15
Geographic Filing Trend
Chart: 
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Total | 4 | 1 | 10 | 21 | 26 | 26 | 106 | 76 | 40 | 7
# Graphs were prepared based on the analysis of application year for all published applications (family expanded data)
# Geographic Filing Trend analysis was done based on the application country.
Global patent filing trend analysis shows a consistent rise in the number of patent applications filed during year 2007-2012, followed by a dip in year 2013-2015. Highest rise was observed in the year from 2011-2012. Maximum number of applications were filed from WO, followed by US and CN jurisdictions.

## Slide 9: Top Assignee - Last Ten Year Filing Trend
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
PROCTER & GAMBLE | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 5 | 1 | 1 | 0
EVIAN EAUX MINERALES | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 3 | 3 | 0 | 0
CANON | 0 | 1 | 0 | 1 | 2 | 2 | 0 | 1 | 1 | 0 | 0
FURANIX TECHNOLOGIES | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 3
TORAY | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0
COCA COLA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0
DU PONT DE NEMOURS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 1 | 0
NOVAMONT | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0
ZHEJIANG UNIVERSITY | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 0
CARBIOS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 0
CHANGCHUN APPLIED CHEMISTRY | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
SULZER | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0
Filing trend of last 10 years for top 13 Assignees (based on representative family members) show a significant rise in filing from 2010-2012 with NOVAMONT leading the pack in 2010, and P&G in 2011 and 2012.
Insights
No. of patent applications filed
# Graph was prepared based on the analysis of application year for published applications (based on the representative family numbers)

## Slide 10: Publication Trend - Overall
Chart: 
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Total | 2 | 6 | 10 | 9 | 22 | 46 | 67 | 89 | 66
Global patent application publication trend presents a significant increase in the number of publication during last decade with its peak at 2014 which suggests significant filing during 2010-2013. Total number of patents published in 2015 may increase till the end of the year.
Insights
Publication Year
No. of
Published
Applications
# Graph was prepared based on the analysis of publication year for all published applications (family expanded data)

## Slide 11: Overall Top Assignees
Procter & Gamble is among leading patent filers in PEF Technology, followed by Canon, which also has a significant patent portfolio.
Insights
Chart: 
| PROCTER & GAMBLE | CANON | DU PONT DE NEMOURS | NOVAMONT | FURANIX TECHNOLOGIES | EVIAN EAUX MINERALES | NOVAMONT | TORAY INDUSTRIES | INNOVIA FILMS | EASTMAN CHEMICAL
Count | 74 | 37 | 23 | 23 | 18 | 18 | 14 | 13 | 10 | 10
No. of
Published
Applications
# The graph was prepared taking into considerations all Mergers & Acquisitions.

## Slide 12: Top Inventors
Chart: 
| TANAKA YUICHIRO (CANON) | MCDANIEL ANDREW (PROCTER & GAMBLE) | COLLIAS IOANNIS (PROCTER & GAMBLE) | REUTENAUER PHILIPPE (EVIAN EAUX MINERALES) | COLLOUD ALAIN (EVIAN EAUX MINERALES) | DAM ADRIANUS (FURANIX TECHNOLOGIES) | KELLETT PATTI JEAN (PROCTER & GAMBLE) | OKUBO TAKURO (TORAY INDUSTRIES)
 | 4 | 2 | 2 | 2 | 2 | 2 | 2 | 1
Insights
As evident, Tanaka Yuchiro from canon is among leading inventors in PEF Technology. Number two position is shared by inventors from P&G, Evian Eaux and Furanix.
No. of
Published
Applications

## Slide 13: Top International Patent Classifications (IPCs)
Chart: 
| C08G 63/16 | C08G 63/181 | C08G 63/78 | C08G 63/42 | Others
count | 6 | 3 | 3 | 3 | 12
Chart: 
| C07D 307/46 | C07D 307/68 | C07D 493/04
count | 3 | 3 | 1
Chart: 
| B32B 27/08 | B32B 27/36 | B32B 27/18 | B32B 05/00 | B32B 03/10 | B32B 05/02
Total | 3 | 1 | 1 | 1 | 1 | 1
Maximum number of applications filed during 2010-2015 correspond to IPC class C08G relating to ‘macromolecular compounds obtained otherwise than by reactions only involving carbon-to-carbon unsaturated bonds’. Amongst applications filed in C08G, 22% of applications were filed in technology of sub-class C0863/16 which relates to ‘Dicarboxylic acids and dihydroxy compounds’. Second highest number of applications were filed in the technology covered by IPC class B32B which relates to ‘layered products, i.e. products built-up of strata of flat or non-flat, e.g. cellular or honeycomb, form’. Amongst applications filed in B32B, 37% of applications were filed in technology of sub-class B32B 27/08 which relates to the ‘Organic chemistry; Heterocyclic Compounds; Carbon atoms having three bonds to hetero atoms with at the most one bond to halogen’.
Chart: 
| C08G | B32B | C07D | B65D | C08L | Others
count | 27 | 8 | 7 | 7 | 6 | 30
Chart: 
| B65D 01/02 | B65D 21/02 | B65D 35/28 | B65D 81/00 | B65D 85/84
count | 3 | 1 | 1 | 1 | 1
Chart: 
| C08L 67/02 | C08L 03/00 | C08L 67/06 | C08L 67/04
count | 3 | 1 | 1 | 1
Insights
# For IPC sub-class definitions please refer to Appendix 2.

## Slide 14
Chart: 
| US | CN | JP | WO | EP | NL | IT | DE | FR | BR | GB | KR | MX | SG
COUNT | 30 | 11 | 11 | 10 | 7 | 4 | 3 | 2 | 2 | 1 | 1 | 1 | 1 | 1
Chart: 
| PROCTER & GAMBLE | TORAY PLASTICS | DU PONT DE NEMOURS | FURANIX TECHNOLOGIES | KRIEGEL ROBERT | Others
COUNT | 12 | 2 | 2 | 2 | 2 | 10
Chart: 
| CHANGCHUN APPLIED CHEMISTRY | ZHEJIANG UNIVERSITY | UNIVERSITY JIANGXI NORMAL SCIENTIFIC & TECHNOLOGY | SUZHOU UHNHI CHEMICAL | DALIAN INSTITUTE OF CHEMICAL PHYSICS | JIANGNAN OF UNIVERSITY | NANJING UNIVERSITY OF TECHNOLOGY
count | 3 | 3 | 1 | 1 | 1 | 1 | 1
Chart: 
| CANON | HITACHI | TORAY INDUSTRIES | FUJIFILM
count | 8 | 1 | 1 | 1
Geographic Origin of Innovation
Insights
Analysis of Geographic Origin of Innovation demonstrates that maximum number of innovations originates from US followed by CN and JP jurisdictions. P&G contributes to maximum number of innovations originating from US. Universities and CHANGCHUN APPLIED CHEMISTRY in particular contributes to maximum number of innovations originating from CN. Canon contributes to maximum number of innovations originating from JP.
# The graph representing Geographic origin of innovation was prepared based on the analysis of priority country
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch

## Slide 15: Key Technological Trends
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch

## Slide 16: Applications of PEF
Chart: 
| FIBRES AND FIBROUS WEBS | BOTTLES | DISPOSABLE ABSORBENT ARTICLE | PACKAGING PRODUCT | FILMS
 | 9 | 8 | 4 | 10 | 5
Chart: 
| PROCTER & GAMBLE | FURANIX TECHNOLOGIES | TORAY PLASTICS | DU POINT
FIBRES AND FIBROUS WEBS | 3 | 1 | 4 | 1
Chart: 
| EVIAN EAUX MINERALES | SUZLER CHEMTECH AG
BOTTLES | 7 | 1
Chart: 
| TORAY PLASTICS | CRYOVAC | UNIV NANJING
FILMS | 2 | 1 | 1
Chart: 
| PROCTER & GAMBLE
DISPOSABLE ABSORBENT ARTICLE | 4
Insights
Maximum percentage of applications were filed where PEF is used in packaging materials, followed by this is fibers and fibrous webs where second highest number of applications were filed relating to PEF. Procter & gamble is the main player in the applications directed towards using PEF in the packaging material. Toray is dominating applicant in the applications directed towards using PEF in the fibers and fibrous webs. Evian Eaux and Toray are having maximum percentages of applications filed against their names in the field of bottles and films respectively. Procter & Gamble is the only player who has filed patent applications which are directed to using PEF in disposable articles.
Chart: 
| PROCTER & GAMBLE | SUZLER CHEMTECH AG | PEPSICO
PACKAGING PRODUCT | 4 | 2 | 1

## Slide 17: PEF Compositions/Derivatives with desired properties
PEF or its Derivative
Ethylene
Glycol +
Diethylene
Glycol (DEG)
2-amino-2-methyl-1,3-Propanediol (AMPD) + Ethylene Glycol
Variations in Diol components to get PEF or its different derivatives
PEF with Desired Properties
US9102793
US8981037
Canon
Canon
Mixing components in specific ratio to get Polymers having specific melt flow index
US8846825
Novamont
CN103502303
Toray
Different Technologies to achieve PEF with desired properties
Mixing components in specific ratio to get Polymers having specific melt flow index
17

## Slide 18: Patent Portfolio Analysis
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch

## Slide 19: Patent Portfolio Analysis – Furanix (Avantium)
US20110282020
Process of preparing PEF having a 2,5-furandicarboxylate moiety
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Process for preparation of PEF
US20140336349
US20110282020
WO2015137804
WO2015142181
WO2015137805
Application
in Fibres
WO2014204313
Process for Recycling
US9073886
Company Profile
Avantium is a leading technology company specialized in the area of advanced catalytic research with groundbreaking innovation as its primary goal. It achieves this through two distinct propositions: Catalysis and YXY.
Technological Dissection of Patent Portfolio
Chart: 
| Polyesters having FDCA and diol content | Fibre composition having PEF | Recycling of PEF
 | 5 | 1 | 1

## Slide 20: Patent Portfolio Analysis – Furanix (Avantium)
Announcement of Avantium – Rhodia partnership
Avantium – Solvay to jointly develop a next generation of green high-performance polyamides
2011
Avantium announced partnership with ALPLA and DANONE
Avantium closed a financing
round of $50 million from a consortium of Swire Pacific, Coca-Cola, DANONE, ALPLA, and existing shareholders
Avantium plans to start commercial production of FDCA and PEF in 2016 through a 50,000 tons/year plant
Avantium completed a $36M million financing
Avantium entered in agreement with Coca-cola for production of bio-based polymers
Key developments
For sources of information, please refer to Appendix 1
2012
2012
2014
2016

## Slide 21: Patent Portfolio Analysis - Furanix (Avantium)
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Patent No. | Novel Features
US9073886 | A process for the depolymerization of a furandicarboxylate containing polyester, which process comprises reacting the polyester with an alcohol or water in the presence of a depolymerisation catalyst to yield a product comprising a furandicarboxylate compound and diol.
US8338626 | A method for the manufacture of ethers of 5-hydroxymethylfurfural by reacting a glucose-containing starting material with an alcohol, selected from methanol, ethanol and mixtures thereof, in the presence of a catalytic or sub-stoichiometric amount of an acid catalyst
IN265547 | Method for the manufacture of ethers of 5-hydroxymethyl furfural by reacting a fructose and/or glucose-containing starting material with an alcohol in the presence of a catalytic or sub-stoichiometric amount of a heterogeneous or homogeneous acid catalyst, wherein water is present as solvent in addition to the alcohol, and wherein the method is performed in a continuous flow process at a temperature from 125 to 300 C.
CA2644409 | Method for the manufacture of ethers of 5-hydroxymethyl furfural by reacting a starting material containing at least one of fructose and glucose, with an alcohol in the presence of a catalytic or sub-stoichiometric amount of a heterogeneous or homogeneous acid catalyst, wherein water is present as solvent in addition to the alcohol, and wherein the method is performed in a continuous flow process at a temperature from 125 to 300 .deg.C
EA021670 | Method for the manufacture of 5-hydroxymethylfurfural ethers by reacting a fructose and/or glucose-containing starting material with an alcohol selected from methanol and ethanol in the presence of a catalytic or sub-stoechiometric amount of a heterogeneous or homogeneous acid catalyst
JP5738517 | Method for the manufacture of 5-alkoxymethylfurfural derivatives by reacting a glucose-containing starting material with an alcohol in the presence of a catalytic or sub-stoechiometric amount of acid catalyst.
Key Patents:
# All granted patents were analysed irrespective of their INPADOC families.

## Slide 22: Patent Portfolio Analysis - Procter & Gamble
Chart: 
| In fibrous webs | In disposable absorbent as polyester | In Packaging
 | 3 | 4 | 4
Application in Disposable Articles
EP2685951
Application in Packaging Materials
US20140377512
EP2697062
Application in Fibrous Webs
US20130023608
EP2668105
EP2763908
US20120238170
EP2685952
US20120238982
US20120238979
US20120237718
Company Profile
Procter & Gamble Co., also known as P&G, is an American multinational consumer goods company which is active into areas such as beauty care, baby, feminine, and family care, fabric and home care, health and grooming. It is mainly active into Europe, America, IMEA and Asia.
Technological Dissection of Patent Portfolio

## Slide 23: Patent Portfolio Analysis - Procter & Gamble
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Key Patents:
Patent No. | Novel Features
CN103429278 | A disposable absorbent article having a structured fiber web using ASTM D6866-10, from about 10% to about 100% by Method B biobased content
US8657596 | An apparatus comprising two intermeshing counter-rotating rolls that form a nip there between, said apparatus comprising: a) a generally cylindrical first roll; and b) a generally cylindrical second roll
US8871319 | A flexible barrier package wherein the package exhibits a lamination strength of sealant to outer substrate of at least about 1.0 N per 25.4 mm of sample width after the package is filled to three-quarters of its volume with a laundry powder composition a and placed in a room at 50% relative humidity (RH) at 55° C. for at least about one month
# All granted patents were analysed irrespective of their INPADOC families.

## Slide 24
Patent Portfolio Analysis- Evian Eaux Minerales (Danone)
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Bottles
EP2855288
WO2014101956
WO2014101957
EP2890544
WO2015087101
WO2015015243
EP2890727
Chart: Bottles with specific properties
Used to make bottles having specific properties. | 7
Company Profile
Societe des Eaux Minerales d'Evian SA provides bottled mineral water. The company was incorporated in 1970 and is based in Evian-les-Bains, France. Societe des Eaux Minerales d'Evian SA operates as a subsidiary of Danone.
Technological Dissection of Patent Portfolio –
Application of PEF
# No granted patents filed between year 2005-2015 are assigned to Evian Eaux Minerales.

## Slide 25: Patent Portfolio Analysis - Canon
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
PEF Composition/Blend
EP2252645
Application in Film
US20120258299
US20120065356
US20090043018
US20100184900
US20100184888
Process of preparation of modified PEF
US20090124763
US7985788
Company Profile
Canon Inc. is a Japanese multinational specialized in the manufacture of imaging and optical products. Reportedly at the beginning of 2015, Canon was the tenth largest public company in Japan when measured by market capitalization.
Chart: 
| PEF Composition/Blend | Application in Film | Process of preparation of modified PEF
 | 6 | 1 | 1
Technological Dissection of Patent Portfolio

## Slide 26: Patent Portfolio Analysis - Canon
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Key Patents:
Patent No. | Novel Features
US8143355 | Reacting a furandicarboxylic acid compound with the polyhydric alcohol presence of an organometallic compound selected from the group consisting of tin, lead and titanium or a tetravalent hafnium
US9102793 | A polyester resin having a number average molecular weight is 100,000 to 120,000
US8981037 | A polyester resin wherein a glass transition temperature of the polyester resin is 93° C. or more to 109° C. or less, and wherein the polyester resin has a number average molecular weight of 31,000 to 160,000
# All granted patents were analysed irrespective of their INPADOC families.

## Slide 27: Patent Portfolio Analysis – Toray Industries
TORAY
INDUSTRIES
US20140004286
Balloon made from a laminate film bio-based PEF homopolymer
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Application in Disposable Articles
EP2685951
Application in Packaging Materials
US20140377512
EP2697062
Application in Fibrous Webs
US20130023608
EP2668105
EP2763908
US20120238170
EP2685952
US20120238982
US20120238979
US20120237718
Company Profile
Toray Industries, Inc. is a multinational company headquartered in Japan was initially into fibers and textiles, as well as plastics and chemicals. The company’s presence can also be felt in the areas such as pharmaceuticals, biotechnology and R&D, medical products, reverse osmosis membranes, electronics, IT-products, housing and engineering, and other advanced composite materials.
Chart: 
| PEF Composition/Blend | Application in Film | Process of preparation of modified PEF
 | 6 | 1 | 1
Patent No. | Novel Features
CN103502303 | Use of 1,2-propanediol with a content of 45-IOOO ppm glycol.
# All granted patents were analysed irrespective of their INPADOC families.
Technological Dissection of Patent Portfolio

## Slide 28: PEF Recycling Technologies
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch

## Slide 29: PEF Recycling Technologies
TORAY
INDUSTRIES
US20140004286
Balloon made from a laminate film bio-based PEF homopolymer
US20130344345
PEF is used to make biaxially oriented bio-based polyester window films and laminates
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Chemical/ Thermal Recycling Technologies
Enzymatic Recycling Technologies
Carbios -
WO2015067619
WO2015097104
WO2014079844
IBM - WO2015056377
Furanix - WO9073886
Figures estimate that around ten million tons of plastic bottles need to be recycled.
Currently, less than 10% of collected plastic is recycled.
Current recycling processes are limited to only a few types of plastic waste which :
means materials to be recycled must have same components;
makes it difficult to recycle complex plastics that combine a mixture of different polymers
requires chemical or thermal recycling processes that make it impossible to retrieve same characteristics as the original product.
Shortcomings of Current Chemical/Thermal Recycling Technologies
For sources of information, please refer to Appendix1

## Slide 30: Chemical/Thermal Recycling - Technological Advancements
WO2015056377 by IBM
PEF
Alcohol having 2 to 5 carbons, an amine organocatalyst, 150 to 250° C
High purity beverage bottle grade polymers
PEF
Water or alcohol
(from 1 to 12 carbon atoms)
Depolymerisation catalyst
(an acid catalyst, a metal compound or a base)
Furandicarboxylate compound + diol
US9073886 by Furanix (Avantium)

## Slide 31: Carbios – Foray into Enzyme based Recycling Technology
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
TORAY
INDUSTRIES
Polymer modifying enzyme
(hydrolase or oxidase)
WO2015097104
PEF
Depolymerase
having binding affinity to PEF
Recovered monomers which may be reprocessed to polymers
US20140004286
Balloon made from a laminate film bio-based PEF homopolymer
US20130344345
PEF is used to make biaxially oriented bio-based polyester window films and laminates
Enzymes
(cutinase, lipase, esterase)
WO2014079844
PEF
Monomers
For sources of information, please refer to Appendix 1
Carbios has started production at its pilot plant in Saint-Beauzire, France, for biodegradable plastic, with a capacity of 40 kilograms per hour, using its exclusive enzyme-based technology. (Date - 27th September, 2015)
Intermediates usable in a methane fermentation process for producing methane
PEF
WO2015067619
In News

## Slide 32: Analysis of Key Granted Patent – Universities and Other Companies
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch

## Slide 33: Granted Patents Analysis – Universities
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Patent No. | Novel Features
CN102453242 (Dalian Institute of Chemical Physics) | A Sb2O3 catalyst and esterification reaction parameters under nitrogen at a temperature of 130-180 ° C, time l-8h; the reaction pressure 2-15mmHg, a temperature of 190 -280 ° C, time is 0.5-8h
CN102276812 (CHANGCHUN APPLIED CHEMISTRY) | Addition of Tetravalent titanium compound catalyst
CN103275288 (ZHEJIANG UNIVERSITY) | A method for preparing a biodegradable multi-block copolymer by reacting L- lactic acid in the presence of an organic acid catalyst at 160-200 ° c under melt condensation 2 -6 hours to a number average degree of polymerization of polylactic acid prepolymer 50-250

## Slide 34: Granted Patents Analysis – Other Companies
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
Patent No. | Novel Features
CN102597050 (NOVAMONT) | A composition comprising derived from aliphatic dicarboxylic acids, biological polyfunctional aromatic acid and diol units biodegradable aliphatic - aromatic polyester, which is derived from a polyfunctional aromatic acid derived units comprise from at least one acid and at least one renewable source of heterocyclic aromatic acid unit
CN102639594 (NOVAMONT) | The composition comprising (A) at least one biodegradable aliphatic-aromatic copolyester comprised between 48 and 70 % by moles and the aliphatic dicarboxylic acids comprise: i from 51 to 95 % by moles of at least one diacid C4-C6; ii from 5 to 49 % by moles (B) at least one polymer of natural origin; wherein the concentration of (A), with respect to (A+B), is > 40 % in weight, and 1.5-10g / 10min melt flow index (MFI)
US8846825B (NOVAMONT) | Mixture having a Melt Flow Index of 1.5-10 g/10 min
US8715524 (FUJIFILM) | A polishing liquid for polishing a barrier layer of a semiconductor integrated circuit comprising: a diquaternary ammonium cation;a corrosion inhibiting agent; and a colloidal silica, wherein the pH of the polishing liquid is in the range of 2.5 to 5.0
FR2985260 (NATURA) | Production of poly (2,5-furan dicarboxylate ethylene) by polycondensation in the presence of at least one catalyst
CN103113577 (SUZHOU UHNHI CHEMICAL) | An alcohol-soluble copolyamide comprising 2, 5-furan dicarboxylic acid, lactam, diamine as raw materials, obtained by melt polymerization
FR2995114 (ARJOWIGGINS SECURITY) | A method of authenticating or identifying a secure document, this document comprising at least one securing or reinforcing element comprising at least one hydrocarbon synthetic polymer derived at least partially from plant resources, process wherein the content of biological material sourced from the element

## Slide 35: APPENDIX 1: Sources
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
http://www.carbios.fr/en/polymers-derived-from-recycling
http://www.foodproductiondaily.com/Innovations/Carbios-starts-production-at-its-pilot-plant-for- biodegradable-plastic
http://www.carbios.fr/en
http://www.coca-colacompany.com/press-center/press-releases/the-coca-cola-company-announces-partnerships-to-develop-commercial-solutions-for-plastic-bottles-made-entirely-from-plants
http://avantium.com/news/2011-2/Avantium-and-The-Coca-Cola-Company-sign-partnership-agreement-to-develop-next-generation-100-plant-based-plastic-PEF.html
http://www.biofuelsdigest.com/bdigest/2014/06/05/avantium-raises-50m-from-coca-cola-danone-swire-and-more-as-all-renewable-pef-plastic-bottles-take-the-spotlight/
http://www.sulzer.com/en/About-us/Our-Businesses/Chemtech
http://www.natura.com.br/www/
http://www.toray.com/news/rd/nr110627.html
http://pubs.acs.org/doi/pdf/10.1021/bk-2012-1105.ch001
http://avantium.com/yxy/products-applications/fdca/PEF-bottles
http://www.novamont.com/eng/news.php

## Slide 36: APPENDIX 2: IPC SUB-CLASS DEFINITIONS
US8981037B2
PEF used in preparation of a polyester resin
EP2235100B1
Resin composition containing polyethylene furandicarboxylate
EP2252645B1
Polyester resin used for producing a molded article
EP2257596B1
Resin composition containing polyethylene furandicarboxylate
CANON
US7741389B2
Resin composition containing a polyalkylene furan dicarboxylate resin and a porphyrin compound
US20120258299
PEF is used in preparation of a polyester resin
US20090124763Method of synthesis, PEF having a furan ring
Patent Searching | Research and Analytics | Patent Prosecution/Preparation Support | Litigation and E-Discovery | IP Valuation | Patent Portfolio Watch
IPC SUB-CLASS | DEFINITIONS
C08G 63/16 | Chemistry; Metallurgy; Organic macromolecular compounds; Their preparation or chemical working-up; Compositions based thereon; Macromolecular compounds obtained otherwise than by reactions only involving carbon-to-carbon unsaturated bonds; Dicarboxylic acids and dihydroxy compounds
C07D 307/68 | Organic chemistry; HeterocyclicCompounds; Carbon atoms having three bonds to hetero atoms with at the most one bond to halogen
C07D 307/46 | Organic chemistry; Heterocyclic Compounds; Doubly bound oxygen atoms, or two oxygen atoms singly bound to the same carbon atom
B65D 01/02 | Performing Operations; Transporting; Conveying; Packing; Storing; Handling thin or filamentary material; Bottles or similar containers with necks or like restricted apertures, designed for pouring contents
C08L 67/02 | Organic Macromolecular Compounds; Their preparation or chemical working-up; Compositions based thereon; Compositions of macromolecular compounds; Polyesters derived from dicarboxylic acids and dihydroxy compounds

## Slide 37: Disclaimer
IIPRD has prepared this sample report as an exemplary report, wherein the content of the report is based on internal evaluation of Patents and Non-Patent Literature that is conducted based on Databases and Information sources that are believed to be reliable by IIPRD. A complete list of patent documents retrieved is not disclosed herein as the report is exemplary but can be shared if desired based on terms and conditions of IIPRD. IIPRD disclaims all warranties as to the accuracy, completeness or adequacy of such information. The above sample report is prepared based on the search conducted on the keywords and other information extracted from the understanding of the Patent Analysts of IIPRD, and subjectivity of the researcher and analyst. Neither IIPRD nor its affiliates nor any of its proprietors, employees (together, "personnel") are intending to provide legal advice in this matter.

## Slide 38: Contact Details
CONTACT DETAILS
Contact Details
Noida (NCR) Office – Head Office
E-13, UPSIDC Site-IV, Behind Grand Venice, Greater Noida, 201308
Contact Person: Tarun Khurana
Contact No.: +91-120-2342010-11/4296878
E-Mail: iiprd@iiprd.com, info@khuranaandkhurana.com
Website: www.iiprd.com | www.khuranaandkhurana.com
California . Delhi . Mumbai . Bangalore . Pune

## Slide 39: About IIPRD
Office- E-13, UPSIDC, Site-IV, Kasna Road, Greater Noida, National Capital Region - 201308, India ,Phone: +91.120.2342010, 3104849, Fax: 2342011, Website: www.iiprd.com, Email: iiprd@iiprd.com
IIPRD is a premier Intellectual Property Consulting and Commercialization/Licensing Firm with a diversified business practice providing services in the domain of Commercialization, Valuation, Licensing, Transfer of Technology and Due-Diligence of Intellectual Property Assets along with providing complete IP and Patent Analytics and Litigation Support Services to International Corporate and Global IP Law Firms.